## Slide 1
Online Plant Performance
Quality
Downtime
OEE
01

## Slide 2
Chart: 
86.0% | 0.86 | 0 | 0 | 0 | 0.14
Chart: 
86.0% | 0.86 | 0 | 0 | 0 | 0.14
Chart: 
86.0% | 0.86 | 0 | 0 | 0 | 0.14
ONLINE PLANT PERFORMANCE
Chart: 
| 0.33333333333333331 | 0.375 | 0.41666666666666702 | 0.45833333333333298 | 0.5 | 0.54166666666666696 | 0.58333333333333304 | 0.625
OEE | 0.812 | 0.8023 | 0.8053 | 0.8141 | 0.8064 | 0.7996 | 0.802 | 0.8014
Target OEE | 0.85 | 0.85 | 0.85 | 0.85 | 0.85 | 0.85 | 0.85 | 0.85
Plant OEE
Availability
86.4%
Performance
92.1%
Quality
97.1%
Main Production
Heel Counter
Chart: 
| GEL | ABG | TWN
 | 2 | 0.6 | 0.7
No of operator
20
No of machine
40
OEE
94%
No of machine
12
A,P, Q of Main Production
Average Cycle Time
Last update: 24th Nov, 8:00 am
Chart: 
| A | P | Q
 | 0.93 | 0.92 | 0.96
OEE
86%

## Slide 3
INSTRUCTION
PLANT OEE (For all category but “Sample, Logo”)
A = 100 * Operating Time (“OT-z4”)/ Planned Processing Time (“PPT3”)
P = 100 * Operating time w/o DT (“NOT4”)/ Operating Time (“OT-z4”)
Q = 100 * Good product (“QCG”)/ Total Output (“B_Output”)
OEE = A*P*Q
MAIN PRODUCTION OEE (except category “Heel Counter, Sample, Logo”)
OEE is similar to the above
Number of Machine: Distinct Count of field “Machine”
Number of Operator: Distinct Count of field “Emp ID”
HEEL COUNTER OEE (only category “Heel Counter”)
OEE is similar to the above
Number of Machine: Distinct Count of field “Machine”
Cycle time: Create a field “Machine” in Running Table, then compute average of cycle time for each machine. Group machine into 4 MC brands (ENG, ABG, TWN and FCS)